## Slide 1: Master & Slave C Code Overview
March 25th, 2021

## Slide 2: Existing Hardware Organization

## Slide 3: Master Micro Duties
Read desired muscle pressures from Matlab.
Write desired muscle pressures to appropriate slave microcontrollers.
Read sensor data from the slave microcontrollers.
Write sensor data to Matlab.

## Slide 4: Master Micro approach
Setup microcontroller in main function.
In a timer interrupt, perform the required duties:
  Read Matlab commands.
  Write Slave commands.
  Read Slave sensors.
  Write Matlab sensors.
Slave information is stored in a data structure: “slave manager”

## Slide 5: A note about functions…
Functions are stored in separate C files.
Function files include:
  Setup_Functions.c
  SPI_Functions.c
  USART_Functions.c
  ADC_DAC_Functions.c
  Conversion_Functions.c
  Pin_Functions.c
  Control Functions
  Encoder Functions
Master & Slave micros have their own versions of each of these files.

## Slide 6: Master Micro: Reading Matlab Commands
Usart_read_matlab_desired_pressures
  Waits for the “start sequence” from Matlab.
  Reads the number of commands to expect.
  Reads each set of command values.
  Stores the desired pressure commands into the slave manager.

## Slide 7: Master Micro: Read / Write to Slaves
Spi_read_write_slave_sensor_specific_command
  Builds a byte array to send to the slave.
  Writes the command ID.
  Writes the sensor ID.
  Writes the command low & high bytes.
  Writes 4 more dummy bytes if we want to read all sensors from the slave.
  Stores the received data in the slave manager.